## Slide 1: Community-Driven Low-Power Wide Area Networking
http://www.openchirp.io

## Slide 2: Low-Power Wide Area Networking (LP-WAN)
IoT is ready to leave the building…
Wide area low data-rate and low-power IoT City Networks
Transmitters can send a few bytes per second over kilometers
Sub 1GHz support deeper building penetration
Existing Technologies
NarrowBand IoT (3G cellular IoT channel)
SIGFOX
LoRaWAN (open standard)
Challenges
User / Service / Device Management
Network Management
Data Representation and Sharing
Plugging in Analytics
Security & Privacy

## Slide 3: What is OpenChirp?
Management Platform for LP-WAN Networks
Web Portal for sharing and managing data sources
Provides Data context, storage, visualization
Developer API and tools
Controller
Sensor
Analytics
Visualization
Access
OpenChirp
Time Series
DB
Meta
Data
Security
Gateway
Gateway
Sensor
Network
Manager

## Slide 4: OpenChirp Concept
Step 2: Grab a LoRa Device
Sounds easy, but there is a lot that needs to be done under the hood…
Step 5: Manage Devices
Step 1: Login using Google ID
Step 4: Register on Web Portal
Step 3: Configure Devices
BLE

## Slide 5
Open-Source Technologies
Scalable PubSub Architecture (MQTT)
Time Series Datastore (InfluxDB)
Data Visualization and Analytics (Grafana)
REST Interface (node.js)
Authentication (OAuth2 integrated with Google)
Meta Data storage and search (MongoDB)
OpenChirp Features
ProtoBuf serialization from end-device to cloud
MQTT for scalable real-time publish subscribe
Bring your own gateway to crowd-source coverage
REST interface for configuration and management
Energy-Efficient Reference Firmware
Intelligent Network Management

## Slide 6: Devices
Transducers
  Sensor / Actuator Name, Unit, Value, Timestamp
Commands
  Shortcut for writing a value to a transducer
  Captures typical ”actuate” requests
  Shareable links
Device Templates
  Package of common transducers / commands with services

## Slide 7: Services
Plug-ins for processing data
  “Stackable” setup a processing pipeline
Sensor Values
ProtoBuf
Raw Data
JSON
EasyBits
LoRaWAN
TSDB
Time Series Database

## Slide 8: Example Services
  Time series data store
    Store data in a TSDB like influx
  LoRaWAN device
    Link a device with a LoRaWAN end-point
  LoRaWAN gateway
    Link a gateway with a LoRaWAN server
  EasyBits
    Link a binary stream to Transducers
  Trigger
    Push a URL on a data event

## Slide 9: Security
Authentication
  Login with google ID for Authentication (OAuth2)
“Thing” Credentials
  Tokens for users, devices and services
  Limited domains
Access Control
  Users / Groups
  Public Links

## Slide 10: OpenChirp Architecture
Sensor
Sensor
Sensor
Services
REST Interface (node)
PubSub Layer. (MQTT)
Auth / ACL Server (OAuth)
Metadata DB (MongoDB)
Timeseries DB (InfluxDB)
Gateway
Web Portal
Apps
Tools
Data Logger
Gateway
Gateway
LoRaWAN Server
Data flows
HTTP REST
Publish-Subscribe
FieldBus Protocol
Wire Protocol
Auth Protocol
(optional)
Actuator
Actuator
Sensor
Sensor
Sensor

## Slide 11: Pilot Deployments
1-λ separated 5.5dBi 902MHz ~ 928MHz
Rooftop Gateway

## Slide 12: CMU LoRa Gateway
SDR
32-Chan Concentrator (x2)
GPS
RPi 3
PoE
MultiTech AP2 (x8)
stackable

## Slide 13: Campus Coverage

## Slide 14: Building Penetration
9 Floor poured concrete building

## Slide 15: LoRa Devices on Campus
LoRaBug
  Open environmental sensor
  Monitors environment in remote indoor areas
Laser Ranger
  Time-of-flight laser ranger
  Monitors structural deflection over time
Occupancy Sensing
  Measure people traffic across spaces
Water Heater Controller
  Demand-Response peak shifting

## Slide 16: LoRaBug – Sensing Platform
SX1276
LoRa Radio
TI CC2650 ARM M3
BLE + 802.15.4
General Purpose
Sensor Header
USB
Sensor Board: Light, Temperature, Accelerometer, Magnetometer, Rate Gyro, Humidity, LEL, Water Contact, Pressure, Audio, PIR motion, 8x8 FLIR imager
5 years @ 15 min

## Slide 17: Laser Monitoring
Range: 150m
Resolution: 1mm
Accuracy: 2mm
Lifetime: 5 years @ 15min

## Slide 18: Bridge Monitoring Example

## Slide 19: Campus Occupancy Sensing
Door Frame Sensor

## Slide 20: GridBallast – Water Heaters
Electric Water Heater Controller
- Learns Grid load profile (Voltage Frequency / ADR)
- Learns User Patterns
- Platform for Demand Response Algorithms
WiFi, BLE and Lora

## Slide 21: Research Thrusts
Network Management
  Automatic configuration with Bring Your Own Gateway model
  Mix of Towers (Macro-cell) and Home APs (Micro-cell)
  Decoupling Data / Control Plan to create “OpenFlow” of LP-WAN
  Security
Whitespace Offloading
  Integrate our framework with FCC database for WS registration
  Dual-mode MAC layer
Localization
  Collaborative localization with APs and Peers
  Improved performance based on RF-modeling and geometry constraints
Application Drivers
  Campus sensing
  Energy-efficient client support

## Slide 22: Thanks, Questions?
http://www.openchirp.io
For more information contact:
General: openchirp@gmail.com
Prof. Anthony Rowe: agr@ece.cmu.edu